## Slide 1: Roll System Mobile
User Manual

## Slide 2: System Requirement
Server Requirement
Hardware:
Personal computers for developing with the minimum configuration:
CPU Core 2 Duo 2.0GHz, 4GB of RAM, 300GB of hard disk, and internet.
Software:
Opearating System: Window 7
Web Server: Microsoft IIS
Database: Microsoft SQL 2008 R2
Mobile Requirement
Android 4.0 or above
Camera 3.0 Megapixed or above

## Slide 3: Image Data Requirement
Each students must has at least 8 images as training images, for acceptable accuracy.
Chart: Face Recognizer Algorithm Accuracy
| 4 | 6 | 8 | 10
Eigen Face | 0.3205 | 0.4103 | 0.5256 | 0.5513
Fisher Face | 0.4103 | 0.5385 | 0.6538 | 0.7692
LPBH Face | 0.4487 | 0.5385 | 0.5385 | 0.6154

## Slide 4: Image Data Requirement
The image should be clear without too much noise.
Two eyes should be as the center.
The face must look front, or tilt ~5-10 degree.
Gray image is also okay
Example of good image data

## Slide 5: Sample Data Set
Sample data of a student (From 8-20 images), should contains:
70-80% of frontal face, with different brightness, facial expression....
20% of side face, with different brightness.
Example of good sample data set:

## Slide 6: Images should not be used
Avoid using images that:
Too blur, too dark or too bright.
Contains big noise, or error.
The face is covered by something.
Tilt with high degree (>20%)
Example of images should not be used

## Slide 7: Position & Angle
For small classrooms

## Slide 8: Position & Angle
For bigger classrooms

## Slide 9: Avoid Position & Angle
For small classrooms

## Slide 10: Avoid Position & Angle
For bigger classrooms

## Slide 11: Number of picture to take
According to test result, with class of 15-20 students, the number of required image is 4-6 images.
With bigger class, the number of required image is 6-10 images.
Chart: 
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Full Recognize Percent | 0.13 | 0.5409 | 0.833 | 0.9548 | 0.9891 | 0.998 | 0.9997 | 1

## Slide 12: Another requirements
The classroom should has good brightness.
The student should look to front, look at the camera.
Example:

## Slide 13: Another requirements
In some situation, the student on the front cover the face of back students, this lead to lower recognition rate.
Solution for better recognition rate:
Take more images in different angles.
Tell front student to lower their head.
Use the “learning” modules.